MACBOOK AIR 13” REPORT | HENRY TIGHE

Device info:
Serial number	FVHWNY2YJ1WK
Model & year	2017 MacBook Air 13”
CPU & GPU	1.8 GHz dual-core Core i5 - 5350U
RAM	8 GB 1600 MHz DDR3 (soldered)
SSD size	128 GB
OS version	MacOS Monterey, 12.6.2

Work done:
- Full exterior cleaning, including sticker removal, screen and keyboard cleaning
- Upgrade to the most recent update of the last supported OS (Apple updates older OS versions)
- Full interior disassembly and cleaning
- CPU & GPU thermal repaste using new Corsair paste on both
- Speaker cleaning and cleaning of crud from the sides of the speaker drivers
- Use of System Report application to check for faults
- Full wipe of device for next user
- After work performed: computer back in my possession, wiped and disk erased
- Attempted to reinstall MacOS Monterey, however errors presented in EFI and Recovery mode
- Apple Store completed Genius Bar request to reinstall Monterey
- Computer repasted with Corsair thermal paste and cooling system opened and reinserted
- Installed BlueBubbles serverside for MacBook to be a server
- Battery management installed to maintain 50% constant charging and device stored, plugged-in
- Monthly restarts maintain laptop

Areas to look out for:
OK, passes test
- Most core functions of the device
- Keyboard & trackpad
Issues resolved but observed before
- Speakers and microphone
- Battery not charging
- Fan stuck at 100%
- Screen not shutting off
Continuing issues
- Spots on mid-left of screen
- Dents/scratches