MACBOOK PRO 15” REPORT | HENRY TIGHE

Device info:
Serial number	There are two serial numbers that this computer has: C02QG2BQG8WM is the case serial number; C02ST2YRG8WL according to logic board ID
Model & year	Mid-2015 15” Retina MacBook Pro
CPU & GPU	i7-4980HQ/Intel Iris Pro & AMD R9 M370X 2 GB (dedicated card)
RAM	16 GB 1600 MHz DDR3 (soldered)
SSD size	512 GB PCIe 3.0 NVMe SSD
OS version	MacOS Monterey mainly (in work done notes)

Work done:
- Computer ordered from eBay in water-damaged, for parts condition
- Startup verified through an external monitor, KB, and mouse; checked diagnostics for problem components
- Ran overnight to update to MacOS Monterey
- Exterior cleaning
- Took out motherboard and most parts inside the case (excluding microphone, battery and trackpad)
- Removed display, took off clutch cover and inspected
- Ordered a refurbished logic board, new keyboard, and new backlight
- Removed keyboard and keyboard backlight previously riveted in
- Replaced keyboard and screwed it in to holes previously occupied by rivets
- Replaced keyboard backlight with new unit
- Rebuilt display
- Replaced logic board with a refurbished unit
- Rebuilt computer sufficiently to test
- Observed problems connecting webcam to logic board; keyboard and trackpad not working
- Reconnected keyboard and trackpad; issues fixed
- Ordered a new logic board and requested refund for faulty one
- Received and installed new logic board
- Completely reassembled and tested computer
- Observed sunken keyboard issue near fn and inverted-T arrow keys; custom designed and 3D printed an internal brace for the arow keys, which fixed the issue
- No fixes available for fn key
- Shipped refunded board in (seller did not want back) in addition to original logic board; received $100 credit at iFixit
- Cleaned device and installed residual updates
- After work performed: installed MacOS Ventura with OpenCore; was forced to uninstall and reinstall Monterey after issues with broken AMD, Intel and display drivers through Recovery mode and a previous backup
- Installed MacOS Sonoma in Sep 2023, needed to reset again due to incorrect OS version selected. I picked the beta and the machine would black-screen and kernel panic upon login.
- Additionally, there have been instances when the display backlight failed, necessitating an emergency reseed of the control cable, kernel panics, and crashes/refusing to charge. All these issues have been resolved but occasionally reappear.
Areas to look out for:
OK, passes test
- Display
- Core CPU/GPU/RAM/SSD functions
- POST/boot and normal use
Issues resolved but observed before
- Webcam issues
- Microphone not working
- Speakers not working
- Keyboard and trackpad not working
- Display not working
Issues that happen randomly/pop up
Unable to enter long-term (>3h) sleep state without shutdown
Continuing issues
None